## Slide 1: Digital Electronics and Computer Organization Lab Course Code: CSE207

## Slide 2: Experiment 1
Simulation and working of all Logic gates
www.circuitverse.org (as a simulator)
Vlab.co.in (http://de-iitr.vlabs.ac.in/List%20of%20experiments.html) Virtual Lab tour

## Slide 3: Gates and Truth tables
AND gate
OR gate
NOT gate

## Slide 4
NAND gate
NOR gate

## Slide 5: Vlab Tour
Working of gates using Simulator
Schematic diagram of each gate

## Slide 6: Circuitverse.org
Launch Simulator
Simulate all the logic gates

## Slide 7: Lab File
Experiment No.:
Aim: Simulation of all Logic Gates
Platform/Tool used: Circuitverse.org simulator
Theory: include symbols and truth table of all gates; write IC number of each gate
Simulated Output: Simulated output snapshots on circuitverse
Result: The logic and universal gates were verified

## Slide 8: Practice Problem
Solve using K-Map and simulate using circuitverse.org
Simplify the following Boolean function in sum-of-products form by means of a four-variable map. Draw the logic diagram with (a) AND-OR gates; (b) NAND gates.
F(A, B, C, D) = ∑ (0, 2, 8, 9, 10, 11, 14 , 15)
F= AB’+AC+B’D’

## Slide 9: F(A, B, C, D) = ∑ (0, 2, 8, 9, 10, 11, 14 , 15)

## Slide 10: Thank you